## Slide 1: Agorà dell’acqua e dei beni comuni Roma, 7-8 Novembre 2015
David Sánchez Carpio
Food & Water Europe
Dal ciclo integrale dell’acqua alla difesa dei territori: verso la COP21 di Parigi
FRACKING
Notes: explore the link between water and climate change, as well as presenting/discussing concrete solutions to protect water resources.
e’ll try to insist on the importance of upstream/control at source approaches to reduce pollution
You may talk about the COP21

## Slide 3: Impacts of shale gas
Why are so many groups opposed to fracking and calling for a ban on fracking?
Notes: What is the difference between conventional and unconventional oil & gas?

## Slide 4: Impacts of shale gas
Number of wells needed

## Slide 5: Impacts of shale gas
IEA: “Be ready to think big”
Notes: Distance between well pads = 3 kms
On pages AP3-90 to AP3-93, the UBA report outlines what is needed to extract shale gas from an area of 260 km2 (~15 by 17 km) over a period of 10 years.
144 well pads (one per every 2 square km!)
864-1440 wells (assuming 6-10 horizontal drills /pad)
8640-14.400 frack jobs (assuming 10 fracks/lateral well)
12-23 million cm3 of fresh water (based on a recycling rate of 75% (which I think is highly optimistic)) ... that is billions and billions of liters of water!
Andy Gheorghiu pointed out that the UBA report (page AP7-100) outlines what will be required to recover the technically recoverable reserves of shale gas in Germany, estimated to be 0,7-2,3 tcm.
an area of 9.300 km2
at least 4000 well pads (each requiring 12.000-48.000 truck movements (page AP7-41))
48.000 wells (or 36 times the scenario outlined above)
assuming this scenario actually happens, this is 'only' equivalent to 10-15 years of Germany's annual gas consumption.

## Slide 6: Climate impacts of (shale) gas
Carbon footprint of natural (shale) gas?
Gas-fired plant offers climate benefit, compared to efficient coal-fired plants
  Only if leakage rate is ~ 3% from well to power plant
  Higher levels of fugitive methane frequently reported
Notes: BTW, most fracking is for shale oil now

## Slide 7: Air pollution
Local air impact
  Diesel engines for fracking equipment & trucks
  Flaring
  Fracking mobilizes pollutants underground:
    BTEX hydrocarbons
    Hydrogen sulfide
    Radon
Hard to monitor: emissions are time- and site-specific

## Slide 8: Public health impacts
Nearby residents have a higher risk of exposure to benzene
Workers’ health
  Use of silica sand as proppant  silicosis
  Higher rate of work accidents
Large-scale fracking also has social impacts:
  Traffic accidents, housing shortage, etc.

## Slide 9: Water impacts
Millions of liters of water
  15 millions for fracking
  Extra 10 for maintenance
A lot of the water is never recovered (20-90%)
Flowback hard to treat
Well integrity problems: methane contamination in aquifers
Regional impact on water supply
  Competition with households, farmers, industry

## Slide 10: Water pollution
Many pathways possible
  Surface: Spills, leaks & blowouts
  Underground: leaky well casings / well integrity failure
  Long-term effect of abandoned wells?
Challenge of treating large volumes of heavily contaminated waste water
  Need for specialized treatment plants
  Deep well injection … but seismic risks
Notes: Shale gas producers generally only recover 20% of the gas from the shale layers, while
in conventional reservoirs, more than 90 per cent of the gas is normally recovered.5 This
means that – once the shale has been fractured – the reservoir pressure will build slowly
but surely. As the materials used to plug the borehole (e.g. mechanical bridge plugs and
/ or cement plugs) degrade, methane will be able to escape over time and contaminate
underground water supplies.6 Large numbers of wells are required to commercially
extract UFF. Hence, the thousands of abandoned wells from UFF operations pose a
long-term threat to our underground water supplies, as the borehole provides a conduit
between the fractured shale and the aquifers. This

## Slide 11: Fracking Chemicals
Lack of transparency about the chemicals used:
Only 1-5% of overall volume, but …
… large volumes of (toxic) chemicals in fracking fluids
  Gelling agents: e.g. diesel
  Biocides: e.g. glutaraldehyde
  Corrosion inhibitor: e.g. methanol
Scepticism needed about ‘chemical-free fracking
Notes: Hydraulic fracturing fluids usually include:
• Gelling agents to hold the proppant in suspension (eg mixtures of industrial guar gum,
diesel, alkanes/alkenes);
• Gel stabilisers (eg sodium thiosulphate) and gel breakers (eg Ammonium persulfate,
sodium persulfate);
• Friction reducers to ease pumping and evacuation of fluid (eg polyacrylamide, mixtures
of methanol, ethylene glycol, surfactants /fluorocarbon surfactants);
• Diluted acid to dissolve minerals (eg hydrochloric acid, muriatic acid);
• Biocides to prevent bacterial action underground (eg glutaraldehyde, Tetrakis
• hydoxymethyl phosphonium sulfate / THPS, 2-Bromo-2-nitro-1,3-propanediol (Bronopol),
2,2-Dibromo-3-nitrilopropionamide (DBNPA);
• Clay stabilisers to prevent clay expanding on contact with water and plugging the
reservoir (eg tetramethyl ammonium chloride); and
• Buffer fluids and crosslinking agents.
Fracking may also use:
• Corrosion inhibitors (eg formamide, methanol, naphthalene, naptha, nonyl phenols,
acetaldhyde);
• Scale inhibitors (eg ethylene glycols);
• I ron control (eg citric acid, thioglycolic acid);
• pH adjusting agents (sodium or potassium carbonate); and
• various surfactants to affect fluid viscosity (eg isopropanol, 2-Butoxyethanol /2-BE.)
The addition of friction reducers allows fracturing fluids and sand, or other solid materials called proppants, to be pumped to the target zone at a higher rate and reduced pressure than if water alone were used. In addition to friction reducers, other additives include: biocides to prevent microorganism growth and to reduce biofouling of the fractures; oxygen scavengers and other stabilizers to prevent corrosion of metal pipes; and acids that are used to remove drilling mud damage within the near‐wellbore area.

## Slide 12: Community impacts
Impact on local roads
  12.000-48.000 truck movements / well pad
Transport of oil and gas
  Gas: Gathering pipelines + compressor stations
  Shale oil: via rail
    Train derailments
    Concerns about volatility of shale oil due to presence of Volatile Organic Compounds

## Slide 19: EU situation
No commercial, large-scale extraction anywhere in Europe
Only in United States and Canada
Bans/Moratorim in France, Bulgaria, The Netherlands, Germany, Ireland, Scotland, Wales, Catalonia, Basque Country

## Slide 20: Resistance
Occupy land in Zamosc, Poland

## Slide 21: Resistance
Block drilling rig (Balcombe, UK)

## Slide 22: Resistance
Occupy land in Pungesti, Romania

## Slide 23: Resistance
Actions by Greenpeace UK

## Slide 24: Where water, climate and energy meet: Fracking for shale gas & oil
Water (ab)use
  Competes with local water users
Water contamination
  Poor water treatment
  Well failure
  Spills and leaks

## Slide 25: Where water, climate and energy meet: Fracking for shale gas & oil
Shale gas is carbon-intensive fossil fuel
  Fugitive methane emissions
  Not suited as ‘transition fuel’
Land use change
  Drilling 1000s of wells mars landscape.

## Slide 26: Toward COP 21 in Paris
Put fossil fuels extraction / ‘extractivism’ on the agenda
  Ban on fracking, tar sands, Arctic and deep-sea drilling …
Fossil fuel subsidies
Unburnable carbon
Focus on origin of emissions, not just ‘end of pipe’ solutions (e.g. Carbon Capture & Storage)

## Slide 27: Resistance
One month of actions against fracking
1250 groups from 64 countries

## Slide 28
www.foodandwatereurope.org
David Sánchez dsanchez@fweurope.org